## Resampling.jl
## Bathymetry Slope-Based Resampling
This program tests the full sonar bathymetry processing chain, from raw .raw sonar files through slope-aware synthetic resampling. It is designed for development, validation, and diagnostics.

### Slope Estimation

slopes = slopesFromBathymetry(baths, config["slopes"]["krad"])
slopes = computeSlopes(baths, slopes)
Purpose:
- slopesFromBathymetry: Calculate slope magnitude and orientation between adjacent depth points.
- computeSlopes: Optionally load precomputed slopes or assigned constant values

### Slope-Aware Resampling

new_baths = resampleBathymetry(baths, slopes,
    config["slopes"]["srad"],
    config["slopes"]["nrsp"])
Purpose: Augment original bathymetry using slope vectors to simulate new depth/position samples around the real measurements.
- srad: Perturbation radius in meters
- nrsp: Number of synthetic points per real sample

### Export Results

export_file = joinpath(@__DIR__, config["slopes"]["export_file"])
export_slopes(baths, slopes, export_file)
Purpose: Write slope metadata (azimuth, gradient, etc.) to disk for visualization or reuse.

### Diagnostics and Testing Output

println(baths[1].depth[1:15]) # Print original depth samples
println(size(new_baths[1].depth)) # Size of synthetic samples
println(new_baths[1].depth[1:15]) # Preview resampled depths
Purpose: Basic sanity checks for:
- Confirming correct bottom detection
- Verifying expected upsampling
- Validating that synthetic depths stay near realistic values